## Slide 1
IGNISENSE
Smart engine
health diagnostic
A digital twin that finds engine faults, names the failing part, and says how long is left, using nothing but sensor readings.
TEAM REVORA
Physics-informed engine digital twin · runs entirely in the browser
Notes: Welcome. IgniSense is a digital twin of a petrol engine that finds faults from sensor data alone. Everything you'll see runs live in this browser, with no server behind it.

## Slide 2
01 · THE PROBLEM
IGNISENSE · TEAM REVORA
02 / 17
Engines fail. Schedules don't know when.
FIXED-INTERVAL SERVICE
Changes parts that are still good.
Misses the part that fails early.
Says nothing about what is wrong, only that it is time.
CONDITION MONITORING
Watches the engine's own sensors.
Notices a fault while it is small.
Names the part, and estimates the time left.
IgniSense shows how, from sensor readings alone.
Notes: Service on a fixed schedule either replaces parts that are still good or misses a part that fails early. Condition monitoring watches the engine itself. Our project shows how a monitor can do that from sensors alone.

## Slide 3
02 · THE IDEA
IGNISENSE · TEAM REVORA
03 / 17
Two engines. One rule.
PLANT
the "real" engine hidden faults live here
SENSORS
noise, drift, spikes, dropouts
TELEMETRY
one common format for every source
TWIN
what the sensors should read
ANALYTICS
gap → fault, health, time left
THE RULE THAT MAKES IT HONEST
The analytics only ever receive sensor telemetry. The fault lives in a part of the code they are not allowed to import, and a lint rule enforces it. The system cannot cheat by reading the answer.
The gap between what the sensors read and what a healthy engine would read is the evidence.
Notes: Two engines run side by side. The Plant is the real engine and holds the hidden fault. The Twin is a healthy copy of the same physics that only sees the sensors. The gap between what the sensors read and what the twin expects is the evidence. The analytics can't see the fault, and a lint rule enforces that.

## Slide 4
03 · SEE IT LIVE
IGNISENSE · TEAM REVORA
04 / 17
A 3D engine on the same physics
Pistons, rods and crank move by the slider-crank equation, not an animation loop.
Cylinders flash in firing order 1-3-4-2.
Health ring and six subsystem scores update live.
Click any part for its sensors and its math.
Notes: This is the live twin page. The 3D engine is procedural and moved by the same slider-crank equation as the numbers; it is slowed 100 times so you can see it. On the right the health ring and the six subsystem scores.

## Slide 5
04 · THE SIGNALS
IGNISENSE · TEAM REVORA
05 / 17
Every gauge has a ghost
White tick = what a healthy engine would read right now.
Δ turns coloured once the gap leaves the noise band.
A dead sensor shows — —, never zero.
Click any value to see the equation behind it.
Notes: Every gauge carries a ghost: the white tick is what a healthy engine would read right now, at the same speed, load and ambient. The delta turns coloured once it leaves the noise. The tachometer is a car-style dial. Click any number and you get the equation.

## Slide 6
05 · BREAK IT, AND IT SHOWS
IGNISENSE · TEAM REVORA
06 / 17
Inject a fault. Watch it show.
Oil-pump wear injected from the test bench.
The sump and oil gallery pulse red; the health ring drops and turns orange.
The monitor names Lubrication-system degradation from the sensors alone.
Repair, and everything settles back.
Notes: Inject any fault from the test bench. The sump and oil gallery pulse red, the ring drops and turns orange, and the card names the fault. Nothing on screen told the monitor which fault we chose. It found it in the sensors.

## Slide 7
06 · DIAGNOSIS
IGNISENSE · TEAM REVORA
07 / 17
It names the fault, and shows its evidence
Probable fault, severity, and a diagnostic evidence score.
"Why the system thinks this": named symptoms, each colour-coded.
A recommended action and the model's own confidence.
Alerts escalate WATCH → WARNING → CRITICAL, with hysteresis.
Notes: When we inject an oil-pump fault, the monitor names it and lists the evidence. Notice we call it an evidence score, never a confidence percentage, because it is a weighted sum, not a calibrated probability.

## Slide 8
07 · EARLY WARNING
IGNISENSE · TEAM REVORA
08 / 17
It warns before any limit trips
CUSUM adds up small, persistent shifts.
A gap of 1σ never crosses a 3σ limit. CUSUM crosses its limit in about 11 samples.
D² flags an unusual combination of residuals (χ² limit 15.09).
Violet lines mark injections. Diamonds mark alerts.
Notes: CUSUM adds up small persistent shifts. A residual that sits at one sigma never crosses a three-sigma limit, but CUSUM passes its limit in about eleven samples. So the monitor warns before any fixed threshold trips.

## Slide 9
08 · WHICH CYLINDER?
IGNISENSE · TEAM REVORA
09 / 17
One missing pulse points at its cylinder
A misfire repeats every two revolutions: a 0.5× line.
That line's phase names the cylinder.
Torque command rises by exactly 4/3: three cylinders do four's work.
0.5× PHASE → CYLINDER
C1
+45°
C2
+135°
C3
−45°
C4
−135°
Notes: A misfire removes one power pulse every two revolutions. That repeats at half the crank frequency. The cylinders fire 180 degrees of crank apart, which is 90 degrees of phase at half order, so the phase of that half-order line points at the cylinder. And the torque command rises by exactly four thirds.

## Slide 10
09 · SENSOR FAULTS
IGNISENSE · TEAM REVORA
10 / 17
When a sensor lies, physics catches it
0.8 K/s
the fastest coolant can possibly heat: all coolant heat at full load, no cooling
250 K/s
what the reading implied: +25 °C in 0.1 s
300×
over the physical limit, so the sensor failed, not the engine
dT/dt|max = Q_cool,max / C_th = 81 500 W / 100 000 J/K ≈ 0.8 K/s
THE VERDICT ON SCREEN
Coolant sensor fault. The cooling system is not blamed: the other sensors and the Twin agree with each other, and the bad readings are left out of the diagnosis.
Notes: If the coolant reading jumps 25 degrees in a tenth of a second, either the engine did something impossible or the sensor failed. The fastest the coolant can heat is all the coolant heat at full load with no cooling: 81.5 kilowatts into 100 kilojoules per kelvin, so 0.8 K per second. The reading beat that by over 300 times. So we blame the sensor, not the engine.

## Slide 11
10 · SHOW THE MATH
IGNISENSE · TEAM REVORA
11 / 17
Click any number. See the equation.
28 registered equations, each with symbols and units.
Live numbers substituted into the LaTeX.
A check table proves it: ✓ EQUAL to the gauge.
Tested in six engine states.
Notes: Every number has an equation behind it, and you can click it. The drawer shows the chain with today's live numbers, and a check table that proves the result equals the gauge. We test that in six different engine states.

## Slide 12
11 · BLIND CHALLENGE
IGNISENSE · TEAM REVORA
12 / 17
Don't trust us. Pick a card.
Nine sealed fault cards, shuffled inside the simulation.
The page never sees what is on the card.
The monitor names the fault from sensors alone.
Reveal → ✓ CORRECT or not.
Notes: This is the proof it isn't reading the injected fault. A visitor picks a sealed card; the fault is chosen inside the worker, and the page never learns what's on it. The monitor has to name it, and then we reveal.

## Slide 13
12 · HOW LONG IS LEFT?
IGNISENSE · TEAM REVORA
13 / 17
Remaining life, with an honest band
A trend line with a ±2 standard-error band.
Shown only when the trend is significant.
Higher load wears faster, so the life shrinks.
One-click, one-page maintenance report as a PDF.
Notes: The remaining-life estimate is a straight-line trend with a plus or minus two standard error band, shown only when the slope is statistically real. Raise the load and the wear speeds up, so the remaining life shrinks. The one-page report prints to PDF.

## Slide 14
13 · CHECKED, NOT JUST CLAIMED
IGNISENSE · TEAM REVORA
14 / 17
Every number is checked against hand calculation
363
automated tests, all passing
26
live checks on the Validation page
2%
tolerance on every review value
Notes: We don't just claim the physics is right. The Validation page recomputes hand-calculated values live in the browser, and every one passes. There are also 363 automated tests, and every golden number from the research review reproduces within two percent.

## Slide 15
14 · FROM SIMULATOR TO A REAL ENGINE
IGNISENSE · TEAM REVORA
15 / 17
Same analytics, any source
SIMULATOR
built-in plant
CSV REPLAY
recorded runs
ESP32
USB, real sensors
OBD-II
a real car
PHONE
accelerometer
TELEMETRY
one common format
TWIN
healthy reference
ANALYTICS
unchanged for every source
Green = tested end to end. Yellow = built and tested on parsers and simulated streams; real hardware is the next step.
Notes: Every source emits the same telemetry object, so adding real hardware means adding one adapter file. Replay of a recorded CSV is tested end to end and reproduces the diagnosis. ESP32 and OBD-II are tested against parsers and simulated streams, not yet real hardware.

## Slide 16
15 · HONEST LIMITS, CLEAR NEXT STEPS
IGNISENSE · TEAM REVORA
16 / 17
What it is not, and what comes next
LIMITS, STATED PLAINLY
Synthetic telemetry; every value is demo calibration.
Lumped thermal model: one coolant, one oil temperature.
Evidence scores are weighted sums, not probabilities.
Remaining life assumes the load continues.
NEXT
Heat-balance run on the college engine rig, to replace demo calibration with measured values.
ESP32 with DS18B20, MAX31855, a pressure transducer and an ADXL345.
Log real failure data, then evaluate machine learning against our statistics.
Notes: We would rather state the limits ourselves. The values are demo calibration, and the data is synthetic. The next step is a heat-balance run on a real engine rig to replace demo calibration with measured data.

## Slide 17
IGNISENSE
Pick a card.
We'll prove it.
Ask us to inject any fault: the monitor only ever sees the sensors.
TEAM REVORA
IgniSense — Smart Engine Health Diagnostic · all values are demo calibration
Notes: Invite them to pick a card, or to name a fault for you to inject.